## Slide 1: Introduction to Safety Risk Management
NextGen Enterprise Safety Team
Fall 2023

## Slide 2: Overview
DIAAT
  System Descriptions
  Identifying Hazards
  Risk Analysis
  Risk Assessment
  Risk Treatment

## Slide 3: DIAAT - The FAA SRM Process
Describe the System
Identify Hazards
Analyze Risk
Assess Risk
Treat Risk

## Slide 4: Describe the System
Typical Description: 5M Model (Man, Machine, Media, Medium, Mission)
Subject Matter Expert presentations
Object-Oriented & Model-Based Approaches

## Slide 5: Hazard
FAR: A condition that could foreseeably cause or contribute to an aircraft accident
ATO Only: Any real or potential condition that can cause injury, illness, or death to people; damage to or loss of a system, equipment, or property; or damage to the environment.

## Slide 6: Risk Analysis
Determine Severity
Determine Likelihood
Risk: the composite of predicted severity and likelihood of the potential effect of a hazard

## Slide 7: Risk Analysis – Icy Interchange
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage

## Slide 8: Risk Analysis – Icy Interchange
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage

## Slide 9: Risk Analysis – Icy Interchange
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage
Step 1: Determine Severity

## Slide 10: Risk Analysis – Icy Interchange
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage
Step 1: Determine Severity

## Slide 11: Risk Analysis – Icy Interchange
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage
Step 1: Determine Severity

## Slide 12: Risk Analysis – Icy Interchange
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage
Step 1: Determine Severity
Step 2: Determine Likelihood

## Slide 13: Risk Analysis – Icy Interchange
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage
Step 1: Determine Severity
Step 2: Determine Likelihood
conditional probabilities

## Slide 14: Risk Analysis – Icy Interchange
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage
Step 1: Determine Severity
Step 2: Determine Likelihood
conditional probabilities
joint probabilities

## Slide 15: Risk Assessment & Expected Values

## Slide 16: Existing/Historic Risk
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage

## Slide 17: A Proposed Change – Salt
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage

## Slide 18: A Proposed Change – Salt
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage

## Slide 19: Initial Risk
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage

## Slide 20: Accident Mitigation
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage

## Slide 21: Accident Mitigation
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage

## Slide 22: Accident Mitigation
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage

## Slide 23: Severity Mitigation
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage

## Slide 24: Severity Mitigation
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage

## Slide 25: Residual Risk
300K vehicles pass through the intersection per day (1.1B in 10 years)
Icy roads occur about a 25 times per year (75M vehicles in 10 years)
Accidents in 10 years:
  7 Fatal, 12 critical/extensive, 75 serious, 5 minor, 1 no injury/damage

## Slide 26: NextGen Enterprise Safety ANG B-32